## Slide 1: IOT
OIT-11
Gido ten Cate, Bram van Gils, Thijs Spapens, Kieran Marriott

## Slide 2: Internet protocol suite
Application layer – HTTP, TLS/SSL, SSH
Transport layer – TCP, UDP
Internet layer – IP (IPv4 & IPv6)
Link layer MAC(Ethernet & DSL)
Notes: The Internet protocol suite is the conceptual model and set of communications protocols used on the Internet and similar computer networks. It is commonly known as TCP/IP because the foundational protocols in the suite are the Transmission Control Protocol (TCP) and the Internet Protocol (IP).

## Slide 3: Hypertext transfer protocol (HTTP)
Application layer
Structured Text that uses logical links between nodes containing text
GET, HEAD, POST, DELETE
HTTP2 Data compression of HTTP Headers
Plain text
Request
Server response
Notes: The Hypertext Transfer Protocol (HTTP) is an application protocol for distributed, collaborative, and hypermedia information systems.[1] HTTP is the foundation of data communication for the World Wide Web.
Hypertext is structured text that uses logical links (hyperlinks) between nodes containing text. HTTP is the protocol to exchange or transfer hypertext.

## Slide 4: Transport Security Layer (TSL)
Application layer
Replaced Secure Sockets Layer (SSL) which was outdated and insecure
TSL handshake
TLS Handshake
Notes: Transport Layer Security (TLS) – and its predecessor, Secure Sockets Layer (SSL), which is now prohibited from use by the Internet Engineering Task Force (IETF) – are cryptographic protocols that provide communications security over a computer network.[1] Several versions of the protocols find widespread use in applications such as web browsing, email, Internet faxing, instant messaging, and voice over IP (VoIP). Websites are able to use TLS to secure all communications between their servers and web browsers.

## Slide 5: Transmission Control Protocol (TCP)
Transport layer
Provides a reliable, orded, and error-checked stream of data (octets) between applications
Notes: The Transmission Control Protocol (TCP) is one of the main protocols of the Internet protocol suite. It originated in the initial network implementation in which it complemented the Internet Protocol (IP). Therefore, the entire suite is commonly referred to as TCP/IP. TCP provides reliable, ordered, and error-checked delivery of a stream of octets (bytes) between applications running on hosts communicating by an IP network. Major Internet applications such as the World Wide Web, email, remote administration, and file transfer rely on TCP. Applications that do not require reliable data stream service may use the User Datagram Protocol (UDP), which provides a connectionless datagramservice that emphasizes reduced latency over reliability.

## Slide 6: Internet Protocol (IP)
Internet layer
Delivers packets from the host to the destination based solely on the ip addresses in the packet headers
IP Header contains (IP address and other metadata)
Notes: The Internet Protocol (IP) is the principal communications protocol in the Internet protocol suite for relaying packets across network boundaries. Its routing function enables internetworking, and essentially establishes the Internet.
IP has the task of delivering packets from the source host to the destination host solely based on the IP addresses in the packet headers. For this purpose, IP defines packet structures that encapsulate the data to be delivered. It also defines addressing methods that are used to label the datagram with source and destination information.
Historically, IP was the connectionless datagram service in the original Transmission Control Program introduced by Vint Cerf and Bob Kahn in 1974; the other being the connection-oriented Transmission Control Protocol (TCP). The Internet protocol suite is therefore often referred to as TCP/IP.
The first major version of IP, Internet Protocol Version 4 (IPv4), is the dominant protocol of the Internet. Its successor is Internet Protocol Version 6 (IPv6).

## Slide 7: Medium Control Access (MAC)
Link layer
Adressing destination stations (individuals or as groups)
Media Access Control (MAC Adress )